## Slide 1
February 10, 2014
Presented By:
Michael E. Parker, P.E.
Parker Environmental and Consulting, LLC
Hydraulic Fracturing
Best Management Practices Comments and Considerations

## Slide 2: Presentation Outline
API Standards, Practices and Guidance
Comprehensive Gas Development Plan
Disclosure
Location Restrictions, Water Reuse
Well Integrity
Methane in Groundwater
Groundwater Protection
Other Issues and Comments
Questions

## Slide 3: API Standards, Practices and Guidance
±170 API Standards, Practices or Guidance apply
  Equipment and materials
  Facility and system design
  Operational practices
Transparent process
  Proven engineering and operational practices
  Performance based approach
3 Guidance documents developed specifically for Hydraulic Fracturing Operations (HF Series)
  HF-1 Well Construction and Integrity
  HF-2 Water Management Associated with Hydraulic Fracturing
  HF-3 Practices for Mitigating Surface Impacts Associated with Hydraulic Fracturing
HF Series currently being upgraded and adding Community Engagement document

## Slide 4: Comprehensive Gas Development Plan and Disclosure
CGDP
Recommend a two step process:
  Exploration Plan
  Development Plan
More consistent with existing law, which uses exploration permit and development permit approach
Utilize expedited permitting for activities identified and approved in the CGDP
2 year baseline monitoring requirement questionable
Disclosure
BMP does not adequately address complexities of pre-job disclosure
Consider a clearinghouse approach for pre-job disclosure
Post-job disclosure
  FracFocus works
  Incorporate use into rules
Protection of IP is critical throughout the process

## Slide 5: Location Restrictions and Water Reuse
Setbacks
Sound technical basis
  Arbitrary setbacks unreasonably limit development
Flexibility
Consider site specific conditions
Develop in conjunction with mitigation and controls
Water Reuse
90% Reuse requirement will be difficult in some cases
“On-site” reuse requirement is unworkable
  Operations processes and logistics prohibit
  Unintended consequence of larger pads

## Slide 6: Well Integrity
Design basis - groundwater protection, formation isolation, pressure containment.
  Multiple API Standards and Practices apply
Consider earlier failure data in context.
  Not all “FAILURES” are failures.
  Risk characterization critical
  Regulatory issues
  Old wells
Integrity verification and monitoring
  Corrosion protection
  Monitoring
  Diagnostic tools
  Maintenance

## Slide 7: Methane in Groundwater
Methane in groundwater occurs naturally
  40-60% incidence rate (Marcellus)
  Many events historically noted
Well integrity critical
  Cementing procedures – API 65-2
    Cement design and testing
    Well cleaning and preparation
    Centralizer use
    Pumping procedures
  Regular well monitoring

## Slide 8: Groundwater Protection
Contamination scenarios offered are extremely unlikely given operational practices
  Pressure and energy are not applied continuously
  Fracture length studies verify zonal isolation and groundwater protection
Casing and cement are sound, durable barriers
Operators must exercise due diligence
  Identify and ensure wells within AOR don’t pose a risk

## Slide 9: Barnett Shale Groundwater Study
Concerns
  Well selection process not random
  Reference wells not representative
    Too few (9)
    5/9 out of area
    9/9 not in the same aquifer
    Also had elevated levels compared to historical data
  Implied pollution sources not characterized
  Potential for drought impacts appear to be minimized
More questions than conclusions
“…we are unable to determine the ultimate source of these elevated concentrations directly.”
“…our discussion of the source of elevated constituents is speculative…”
“…natural gas extraction activities do not result in systematic contamination of groundwater.”

## Slide 10: Barnett Shale Study Area

## Slide 11: 2011 vs. 2014 Drought Conditions
2011
2014

## Slide 12: Other Issues

## Slide 13
Questions
Michael E. Parker, P.E.
Parker Environmental and Consulting, LLC
ParkerEnC@gmail.com
(832) 581-5474
Drew Cobbs
Maryland Petroleum Council
Cobbsd@api.org
(410) 269-1850
To Learn More:
www.api.org
www.energyfromshale.org
Drilling Video
http://www.youtube.com/watch? v=AYQcSz27Xp8&feature=relmfu
Fracturing Video
http://www.youtube.com/watch?v=7ned5L04o8w